## Slide 1: GPGPU with SYCL
NPRG042 Programming in Parallel Environment
Martin Kruliš

## Slide 2: GPU vs. CPU
CPU
  Few cores per chip
  General-purpose cores
  Processing different threads
  Huge caches to reduce memory latency
    Locality of reference problem
GPU
  Many cores per chip
  Cores specialized for numeric computations
  SIMT thread processing
  Huge number of threads and fast context switch
    Results in more complex memory transfers
Architecture Convergence

## Slide 3: GPU Architecture
Maxwell GPU
Streaming multiprocessor (SM)
CUDA core

## Slide 4: GPU Architecture
Maxwell Architecture
  4 identical parts
    32 cores
    64 kB shared memory
    2 instruction schedulers
  CC 5.0
  SMM (Streaming Multiprocessor - Maxwell)

## Slide 5: GPU Architecture
Volta SM
  7.x CC
  8x tensor core
  (64 FMA/clock each)

## Slide 6: Execution Model
Data Parallelism
  Many data elements are processed concurrently by the same routine
  GPUs are designed under this particular paradigm
  Also have limited ways to express task parallelism
Threading Execution Model
  One function (kernel) is executed in many threads (work items)
  Much more lightweight than the CPU threads
  Threads are grouped into blocks (work groups) of the same size

## Slide 7: Single Instruction Multiple Threads
Single Instruction Multiple Threads
  All cores are executing the same instruction
  Each core has its own set of registers

## Slide 8: SIMT vs. SIMD
Single Instruction Multiple Threads
  Width-independent programming model
  Serial-like code
  Achieved by hardware with a little help from the compiler
  Allows code divergence
Single Instruction Multiple Data
  Explicitly expose the width of the SIMD vector
  Special instructions
  Generated by the compiler or directly written by a programmer
  Code divergence is usually not supported or tedious

## Slide 9: Workload Distribution
Nd-grid and work elements assignment
GPU
Streaming Multiprocessor
Core
nd-grid
work-group
warp
work-item
Assigned to SM
Threads in a warp run in lockstep
The same kernel
Threads (warps) are being swapped quite fast

## Slide 10: Lockstep Execution
Lockstep
  Multiple threads (warp) execute the same instruction simultaneously
  Simplifies the design of the SMs
  The programmer needs to know
    When optimizing the code
    Not expressed explicitly in SYCL
    Cannot rely on that (e.g., for sync.)
  Divergence is possible
    But not very efficient
  Volta significantly loosens lockstep
    Threads may diverge in hardware

## Slide 11: Memory
Global Memory
L2 Cache
Registers
Core
Core
…
Registers
Core
Core
…
…
Host
CPU
Host Memory
SMP
GPU Chip
GPU Device
PCI Express
(60/120 GBps)
~ 30-60 GBps
> 100 GBps and >1000 (HBM2)
L1
Shm
L1
Shm
Private memory
Local memory

## Slide 12: Memory
Host-device transfers
  Implicit (declared by accessors, handled by the scheduler) – no control
  Explicit handler.copy(src, dest);
Registers
  All local variables of the kernel
  Limited size, registry spilling (cached in L1)
Local (shared) memory
  Special memory shared among work-group
  Very fast, used for (manual) caching or data exchange (items in group) auto shm = sycl::accessor<int, 1, sycl::access::target::local>(…);

## Slide 13: Code Example
static auto exh = [](sycl::exception_list l) { for (std::exception_ptr const &e : l){ try { std::rethrow_exception(e); } catch (std::exception const &e) { std::terminate(); } } }; std::vector<int> A, B, C; auto selector = sycl::gpu_selector_v; try { sycl::buffer a_buf(A); sycl::buffer b_buf(B);
sycl::range<1> rng{ A.size() }; sycl::buffer c_buf(C.data(), rng); sycl::queue q(selector, exh); q.submit([&](sycl::handler &h) { sycl::accessor a(a_buf, h, sycl::read_only); sycl::accessor b(b_buf, h, sycl::read_only); sycl::accessor c(c_buf, h, sycl::write_only, sycl::no_init); h.parallel_for(rng, [=](auto i) { c[i] = a[i] + b[i]; }); } q.wait_and_throw(); } catch (std::exception const &e) { // print e and terminate }

## Slide 14: Synchronization (Reminder)
Host side
  queue.wait();
  Events
    Returned by queue operations auto event = queue.submit(…);
    event.wait();
    Events can be passed as dependencies to some operations queue.submit(…, event, …)
In kernel
  Barriers
    nd_item::barrier()
    Only within the work group!
  Atomic operations
    Similar to C++
    auto v = sycl::ext::oneapi::atomic_ref <int,order,scope,space>(a[0]); v += something;
Kernel execution overhead is in the range of μs
Queue can be configured as in-order
Available both for local and global memory, quite efficient (if no collisions)

## Slide 15: Lockstep Implementation
Masking Instructions
  In case of data-driven branches
    if-else conditions, while loops, …
  All branches are traversed, threads mask their execution in invalid branches
    if (threadIdx.x % 2 == 0) {
    ... even threads code ...
    } else {
    ... odd threads code ...
    }
0
1
2
3
4
…
0
1
2
3
4
…

## Slide 16: Reducing Thread Divergence
Work Reorganization
  In case the workload is imbalanced
  “Cheap” load balancing can lead to better occupancy
  Example
    Matrix with dimensions not divisible by warp size
    Item (i,j) has linear index i*width + j
The overhead must not eliminate the gain
Notes: Cheap = the cost of the balancing must not overweight the actual savings.

## Slide 17: Optimizations: Hiding Latency
Fast Context Switch
  When a warp gets stalled
    E.g., by data load/store
  Scheduler switch to next active warp

## Slide 18: Optimizations: Global Memory
Access Patterns
  Perfectly aligned sequential access

## Slide 19: Optimizations: Global Memory
Access Patterns
  Perfectly aligned with permutation

## Slide 20: Optimizations: Global Memory
Access Patterns
  Continuous sequential, but misaligned

## Slide 21: Optimizations: Global Memory
Coalesced Loads Impact

## Slide 22: Optimizations: Local (Shared) Memory
Linear Addressing
  Each thread in warp access different memory bank
  No collisions

## Slide 23: Optimizations: Local (Shared) Memory
Linear Addressing with Stride
  Each thread access 2*i-th item
  2-way conflicts (2x slowdown) on CC < 3.0
  No collisions on CC 3.x
    Due to 64-bits per cycle throughput

## Slide 24: Optimizations: Local (Shared) Memory
Linear Addressing with Stride
  Each thread access 3*i-th item
  No collisions, since the number of banks is not divisible by the stride

## Slide 25: Optimizations: Local (Shared) Memory
Broadcast
  One set of threads access value in bank #12 and the remaining threads access value in bank #20
  Broadcasts simultaneously

## Slide 26: Optimizations: Host-device Transfers
Making a Good Use of Overlapping
  Split the work into smaller fragments
  Create a pipeline effect (load, process, store)

## Slide 27: Heterogeneous Programming
GPU
  “Independent” device
  Controlled by host
  Used for “offloading”
Host Code
  Needs to be designed in a way that
    Utilizes GPU(s) efficiently
    Utilize CPU while GPU is working
    CPU and GPU do not wait for each other
Notes: Remember Amdahl’s Law.

## Slide 28: Discussion