## Slide 1: SIMD

## Slide 2: SIMD
SIMD = Single Instruction Multiple Data
Hardware support
  Vector registers
    wide registers (64-512 bits), interpretation depends on instructions used
    in some architectures, (lower) parts of wide registers act as smaller vector (or even scalar) registers (backward compatibility)
  Vector instructions
    act on vector registers similarly to normal instructions acting on scalar registers
      what humans call vectors, hardware sees as scalars
    logically, each vector instruction performs N mathematical operations at once
      In most cases, the N lanes act independently
    physically, the N operations may be executed:
      all in the same moment, using N hardware units
      in a pipeline, using single hardware unit (usually divided into stages)
      combined, feeding N/K batches into K hardware units
      scalability: different hardware may use different K for the same instruction
    different instructions use different vector elements (double, float, int64,...,int8)
      instructions have different N (therefore K)
      the same hardware (e.g. an adder) is reconfigured into different K’s (e.g. by cutting carry)

## Slide 3: Different processing strategies
N=8, K=4
N=8, K=8
time
Example: Older implementations of AVX
Problem: Cross-lane instructions (e.g. shuffles) cannot pass data between the two halves
Example: Newer implementations of AVX using either a 256-bits wide pipeline or two 128-bit pipelines synchronously
The problem remains visible in the AVX instruction set

## Slide 4: Different lane width
N=8, K=4
N=8, K=8
time
Example: Single-precision FP in AVX
8*32 = 256 bits
Example: Double-precision FP in AVX
4*64 = 256 bits
N=4, K=2
N=4, K=4

## Slide 5: SIMD
Hardware support
  Vector registers
  Vector instructions
  Memory transfers
    in most cases, vector registers must be read/written from/to contiguous blocks of memory
    existence of vector instructions requires widening of internal data paths in CPU
    similarly to arithmetics, one vector may be transferred either at once or as a series of smaller batches (since ultra-wide data paths are expensive)
      the batches (usually) originate in the same cache line – only one cache lookup needed
      even if the data paths were not wider than a scalar, vector transfers would be faster
    there are soft or hard requirements for alignment
      Align to data path width (16/32 bytes in current Intel/AMD CPUs)
      Do not cross cache line boundaries (64 bytes in all current Intel/AMD CPUs)

## Slide 6: SIMD
Software support
  Automatic vectorization by compilers
    The transformation is often non-equivalent wrt. strict language rules
      Explicit permission from the programmer is needed (pragma)
    Advanced transformation methods now called “polyhedral compilation” (e.g. Polly/LLVM)
  Vectorized library code
    Operations on arrays/matrices implemented using vector instructions
  Explicit use of vector datatypes and instructions
    Make use of all instructions available, including peculiarities
    In assembly languages – error prone and often worse than product of compilers
    In higher languages – using intrinsic functions
      Compilers take care of register allocation, addressing, type safety, etc.
  Handling alignment requirements
    All parts (programmers, compilers, libraries) must cooperate to make data properly aligned

## Slide 7: SIMD in Intel/AMD x64
SIMD support in Intel/AMD CPUs
  MMX (Intel 1997)
    64 bits, 8 registers (MM0..7), shared with scalar floating-point unit (x87)
    only integer operations (8/16/32-bit), targeted at audio processing
    AMD 3DNow added some 32-bit floating point support
  SSE (Intel 1999)
    128 bits, 8 registers (XMM0..7), only 32-bit floating point supported
  SSE2-SSE4 (Intel 2001-2007)
    64-bit floating-point and 8/16/32/64-bit integer arithmetics for 128-bit vectors
  x64 (AMD 2003)
    additional 8 registers (XMM8..15) available in 64-bit mode
  AVX (Intel/AMD 2011)
    256 bits, 16 registers (YMM0..15) (only YMM0..7 accessible in 32-bit mode)
    floating point (32/64-bit) operations only
    three-operand instruction format
  AVX2 (Intel 2013)
    integer arithmetics (8/16/32/64-bits) extended to 256-bit vectors
    gather/maskstore instructions

## Slide 8: SIMD in Intel/AMD x64
SIMD support in Intel/AMD CPUs
  AVX (Intel/AMD 2011)
    256 bits, 16 registers (YMM0..15) (only YMM0..7 accessible in 32-bit mode)
    floating point (32/64-bit) operations only
    three-operand instruction format
  AVX2 (Intel 2013)
    integer arithmetics (8/16/32/64-bits) extended to 256-bit vectors
    gather/maskstore instructions
  IMCI (Intel 2012)
    in Intel Knights Corner architecture (aka. MIC aka. Xeon Phi)
    512 bits, 32 registers (ZMM0..31)
    gather/scatter instructions
    mask registers
  AVX512 (Intel 2016)
    in Intel Knights Landing (aka. MIC 2 aka. Xeon Phi second generation)
    in Intel Skylake Purley (2017), Cannonlake (2018)
    most instructions equivalent to IMCI (but different binary encoding)

## Slide 9: SIMD
Advantages of SIMD
  Greater arithmetic throughput
    double-precision multiply on Skylake: 2*4 operations per clock cycle (vs. 2 scalar)
      fused multiply-add (FMA): 2*4 muls + 2*4 adds per clock
    32-bit integer addition on Skylake: 3*8 operations per clock (vs. 4 scalar)
  Greater memory throughput
    Only vector instructions can use the full 256-bit width of CPU-L1 bus
    Vector throughput: 64B loads + 32B stores per clock
      Scalar double-precision throughput: 16B loads + 8B stores
  Greater register file
    scalar x64 integer: 16*64bit = 128 bytes
    scalar extended-double-precision: 8*80bit = 80 bytes
    AVX2: 16*256bit = 512 bytes
    AVX512: 32*512bit = 2048 bytes
      for comparison: Xeon Phi L1 Cache = 64 KB shared by 4 threads = 16 KB per thread

## Slide 10: Vector data types and registers (MMX/SSE/AVX/AVX512)

## Slide 11: Integer registers – 8 bit CPU
FLAGS
PC
1974
Intel 8080
12 B of registers
64 KB addressable memory
A
HL
BC
DE
SP

## Slide 12: Integer registers – 8 bit CPU
FLAGS
PC
1976
Zilog Z80
16 B of (app) registers
64 KB addressable memory
A
HL
BC
DE
SP
IX
IY

## Slide 13: Integer registers – 16 bit mode
AX
BX
CX
DX
SI
DI
BP
SP
FLAGS
IP
1978
Intel 8086
20 B of (app) registers
1 MB addressable memory

## Slide 14: Integer and FPU registers – 16 bit mode
ST
ST
AX
BX
CX
DX
SI
DI
BP
SP
FLAGS
IP
1980
Intel 8086+8087
100 B of (app) registers
1 MB addressable memory
8 80-bit FP registers in co-processor chip (8087)

## Slide 15: Integer and FPU registers – 32 bit mode
this picture is shown with MSB on the left
ST
ST
EAX
EBX
ECX
EDX
ESI
EDI
EBP
ESP
EFLAGS
EIP
1985
Intel 80386+80387
120 B of app registers
4 GB addressable memory

## Slide 16: Integer and FPU registers – 32 bit mode
this picture is shown with MSB on the left
ST
ST
EAX
EBX
ECX
EDX
ESI
EDI
EBP
ESP
EFLAGS
EIP
1989
Intel 80486
120 B of app registers
4 GB addressable memory
The FPU is now on the same chip

## Slide 17: Scalar and vector registers (MMX) – 32 bit mode
this picture is shown with MSB on the left
(lane 0 on the right)
ST
ST
MM0
MM7
64-bit MMX registers were carved from the 80-bit FP registers (x87)
EAX
EBX
ECX
EDX
ESI
EDI
EBP
ESP
EFLAGS
EIP
1997
Intel Pentium MMX
120 B of app registers
4 GB addressable memory

## Slide 18: Scalar and vector registers (MMX/SSE) – 32 bit mode
this picture is shown with MSB on the left
(lane 0 on the right)
XMM0
XMM7
ST
ST
MM0
MM7
64-bit MMX registers were carved from the 80-bit FP registers (x87)
EAX
EBX
ECX
EDX
ESI
EDI
EBP
ESP
EFLAGS
EIP
1999
Intel Pentium III
248 B of app registers
4 GB addressable memory

## Slide 19: Scalar and vector registers (MMX/SSE) – 64 bit mode
this picture is shown with MSB on the left
(lane 0 on the right)
XMM0
XMM7
XMM8
XMM15
ST
ST
MM0
MM7
64-bit MMX registers were carved from the 80-bit FP registers (x87)
RAX
RBX
RCX
RDX
RSI
RDI
RBP
RSP
R8
R9
R10
R11
R12
R13
R14
R15
XMM/YMM8-15 and R8-15 available only in the 64-bit execution mode
RFLAGS
RIP
2003
AMD Opteron
480 B of app registers
1 TB addressable memory

## Slide 20: Scalar and vector registers (IMCI)
ZMM0
ZMM31
this picture is shown with MSB on the left
(lane 0 on the right)
RAX
RBX
RCX
RDX
RSI
RDI
RBP
RSP
R8
R9
R10
R11
R12
R13
R14
R15
RFLAGS
RIP
2010
Intel Xeon Phi
Knights Corner
2272 B of app
registers
per thread
The first Knights Corner
CPUs were derived from a Pentium core converted to 64 bits and had no support for SSE or MMX
ST
ST

## Slide 21: Scalar and vector registers (MMX/SSE/AVX)
this picture is shown with MSB on the left
(lane 0 on the right)
YMM0
YMM7
YMM8
YMM15
XMM0
XMM7
XMM8
XMM15
ST
ST
MM0
MM7
RAX
RBX
RCX
RDX
RSI
RDI
RBP
RSP
R8
R9
R10
R11
R12
R13
R14
R15
XMM/YMM8-15 and R8-15 available only in the 64-bit execution mode
RFLAGS
RIP
2011
Intel Sandy Bridge
736 B of app registers per thread
1 TB addressable memory

## Slide 22: Scalar and vector registers (MMX/SSE/AVX/AVX512)
ZMM0
ZMM7
ZMM8
ZMM15
ZMM16
ZMM31
YMM0
YMM7
YMM8
YMM15
YMM16
YMM31
this picture is shown with MSB on the left
(lane 0 on the right)
XMM0
XMM7
XMM8
XMM15
XMM16
XMM31
ST
ST
MM0
MM7
RAX
RBX
RCX
RDX
RSI
RDI
RBP
RSP
R8
R9
R10
R11
R12
R13
R14
R15
RFLAGS
RIP
K1
K2
K3
K4
K5
K6
K7
AVX512 mask registers
2013
Intel Xeon Phi
Knights Landing
2286 B of app
registers
per thread

## Slide 23: Vector data types (MMX/SSE/AVX/AVX512)
32
32
16
16
16
16
8
8
8
8
8
8
8
8
float
float
double
64
128
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
8
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
32
32
32
32
32
32
32
32
32
32
32
32
32
32
64
64
64
64
64
64
64
128
128
128
float
float
float
float
float
float
float
float
float
float
float
float
float
float
double
double
double
double
double
double
double
AVX512 – 512 bits
AVX – 256 bits
SSE – 128 bits
MMX – 64 bits
epi128/si128
epi64 (signed)
epu64 (unsigned)
epi32 (signed)
epu32 (unsigned)
epi16 (signed)
epu16 (unsigned)
epi8 (signed)
epu8 (unsigned)
DQ
or none
Q
D
W
B
PS
PD
only bitwise and/or/xor and shift instructions
ps
pd
C intrinsic
function suffix
assembler
instruction
suffix (Intel)
this picture is shown in the memory order
(lane 0 on the left)

## Slide 24: Floating-point vector data types (MMX/SSE/AVX/AVX512)
16
16
16
16
float
float
double
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
float
float
float
float
float
float
float
float
float
float
float
float
float
float
double
double
double
double
double
double
double
AVX512 – 512 bits
AVX – 256 bits
SSE – 128 bits
ph
PH
PS
PD
ps
pd
C intrinsic
function suffix
assembler
instruction
suffix (Intel)
Bits shown with MSB on the left; opposite of the memory order:
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
16
pbh
BF16
AVX-512_BF16 - since Cooper Lake (Intel 2020):
AVX-512_FP16 - since Sapphire Rapids (Intel 2023):
E
E
S
E
E
E
E
E
M
M
E
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
E
E
S
E
E
E
E
E
M
M
E
M
M
M
M
M
E
E
S
E
M
E
E
M
M
M
M
M
M
M
M
M
...
E
E
S
E
E
E
E
E
E
E
E
E
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
M
ph = IEEE 754 Half
ps = IEEE 754 Single
pd = IEEE 754 Double
pbh

## Slide 25: Vector instructions (SSE/AVX/AVX512)

## Slide 26: Vector instructions (SSE/AVX/AVX512)
Memory access
  Loads and stores
  In addition, many other instructions may have up to 1 memory operand
Plain arithmetic instructions
  Parallel execution of the same operation in each lane, independently
Conditions and masks
  Support for conditional execution, independently in each lane
Inter-lane arithmetics
  Applying selected operations across lanes
Inter-lane shuffles
  Movement of data between lanes
Conversions
  Changing widths of data; interaction with scalar registers
The list in these slides can never be complete, see the reference:
        https://www.intel.com/content/www/us/en/docs/intrinsics-guide/index.html

## Slide 27: Vector instructions (SSE/AVX/AVX512)
Memory access
  Vector load and stores
      Load/store vector from/to a consecutive block of memory
    load/store - Aligned loads/stores – fault if unaligned to a multiple of 16B
    loadu/storeu - Unaligned load/stores – slower if unaligned
      In older architectures, slower even if aligned – use only if alignment cannot be guaranteed
    stream_load - Non-temporal loads – not stored in caches (where architecture allows)
      To avoid cache pollution when the data will not be read again soon
  Memory arguments of vector instructions
    At most one argument may reside in memory
    In SSE, the memory argument must always be aligned to 16B
    In AVX-enabled CPUs, memory arguments may be unaligned (resulting in slower operation)
      Applies also to SSE instructions, if VEX-encoded (assembler names prefixed by ‘V’)
  When used from C/C++
    The compiler automatically generates loadu/storeu (or memory arguments if AVX is enabled) whenever working with memory operands
    If alignment is guaranteed, explicit load/store to a local variable usually produces faster code

## Slide 28: Vector instructions (SSE/AVX/AVX512)
Memory access and data types
  Formally, a vector load/store of a particular width (128/256/512 bits) just moves the bits between memory and a (XMM/YMM/ZMM) register, independently of the lane size and format
  Physically, floating-point vectors may be routed through different parts of the CPU than integer vectors
    And, in theory, different lane widths may also have different pathways
    This arrangement makes the data closer to the respective hardware units for the following/preceding arithmetic instructions
  Therefore, there are (at least) three kinds of instructions for loads/stores
      And even more intrinsic functions mapped to them
    *MOVDQ(A|U) = *(load|store)[u]_[e]si(32|64|128) = integer loads/stores
    *MOV(A|U)PS = *(load|store)[u]_ps = float loads/stores
    *MOV(A|U)PD = *(load|store)[u]_pd = double loads/stores
  Always use the form of load/store related to the arithmetic instructions which operate on the data
    With intrinsic functions in C/C++, this is enforced by the existence of different data types representing integer/float/double vectors
    In assembly language, there is no enforcement

## Slide 29: Vector instructions (SSE/AVX/AVX512)
Memory access
  Gather/scatter
    Gather available from AVX2, scatter only for AVX512 (and KNC)
    Load/store lanes of a vector from/to individually indexed positions
      Available only for 32 or 64 bit data elements
      Addresses computed by adding a common base address and (the 1/2/4/8-multiple of) an 32/64 bit index in the corresponding lane of a vector register
      Index and data register may differ in size (e.g., _mm256_i32gather_epi64 reads indexes from a 128-bit register and stores to a 256-bit)
    The CPU may perform individual lane loads/stores in parallel
      if they do not hit the same parts of the internal memory buses
      similar to the notion of stride in GPUs but far less massive
    In any case, gather/scatter is slower than contiguous loads/stores
      But faster than a series of scalar load/stores
    Gather:
        for (i in 0..N-1) v[i] = a[c*x[i]]
      c is a constant of 1/2/4/8
    For scatter, individual lanes may be masked by a bit-mask:
        for (i in 0..N-1) if (m[i]) a[c*x[i]] = v[i]
    Beware: If two indexes are identical in the same scatter, the result is undefined
      Use *conflict* instructions (in AVX512CD) to detect, then masking to avoid

## Slide 30: Vector instructions (SSE/AVX/AVX512)
Plain arithmetic instructions
  Parallel execution of the same operation in each lane, independently
        for (i in 0..N-1) c[i] = f(a[i],b[i])
  Integer arithmetics:
    ADD, SUB in 8/16/32/64 bit lanes
    Saturated signed/unsigned ADD/SUB in 8/16 bit lanes
    Shifts in 16/32/64/128 bit lanes
    MUL in 32/64 bit lanes
  Floating-point arithmetics (32/64-bit lanes)
    ADD, SUB, MUL, DIV
    FMA (fused multiply-add)
        d[i] = c[i] + a[i]*b[i]
    DP (dot product) with extension pbh->ps
        d[i] = c[i] + a[2*i]*b[2*i] + a[2*i+1]*b[2*i+1]

## Slide 31: Vector instructions (SSE/AVX/AVX512)
Conditions and masks
  Support for conditional execution, independently in each lane
SSE and AVX
  Comparisons produce all-ones (-1) or all-zeros (0) in each lane
    Only EQ and GT supported for integers, the others must be derived
    All six comparisons supported for floating point
  Conditional expressions are simulated using bitwise AND, ANDNOT, and OR:
    BEWARE: ANDNOT negates the FIRST argument before anding
        // for (i in 0..N-1) e[i] = a[i] == b[i] ? c[i] : d[i]
        cond = cmpeq(a,b) // cond[i] = a[i] == b[i] ? -1 : 0
        left = and(cond,c) // left = cond & c
        right = andnot(cond,d) // right = ~cond & d
        e = or(left,right) // e = left | right
  The three bitwise operators come in three flavors, depending on type
      The reason is the same as for loads/stores
    *P(AND|ANDN|OR) = *(and|andnot|or)_si128
    *(AND|ANDN|OR)PS = *(and|andnot|or)_ps
    *(AND|ANDN|OR)PD = *(and|andnot|or)_pd

## Slide 32: Vector instructions (SSE/AVX/AVX512)
Conditions and masks
  Support for conditional execution, independently in each lane
AVX512
  7 special mask (K) registers containing single bit for each lane
    The number of lanes used depend on the instruction
    Presented as types __mmask[8|16|32|64] in C/C++
  Comparisons produce one bit for each lane
    All six comparisons supported for all types
  Almost all instructions have masked variants
    The instruction is applied for the lanes which have 1 in the corresponding mask operand lane
    In the other lanes, the result register retains the previous value
    Comparison instructions may be masked too – used to simulate Boolean conjunction
  In C/C++ intrinsics, masking is presented in two forms
    mask – two additional inputs: previous value vector src and mask vector k:
        for (i in 0..N-1) r[i] = k[i] ? f(a[i],b[i]) : src[i]
    maskz – one additional input: mask vector k, masked lanes produce zero:
        for (i in 0..N-1) r[i] = k[i] ? f(a[i],b[i]) : 0
  Conditional expressions and statements are simulated using masking:
    The same mechanism is used in GPUs
        // for (i in 0..N-1) e[i] = a[i] == b[i] ? c[i] : d[i]
        cond = cmpeq(a,b) // cond is a mask register
        e = mask_mov(right,cond,left) // e[i] = cond[i] ? left : right

## Slide 33: Vector instructions (SSE/AVX/AVX512)
Inter-lane arithmetics
  Applying selected operations across lanes
  hadd/hsub - Horizontal ADD/SUB (16/32/float/double lanes)
    SSE version:
        for(i in 0..N/2-1) {
        r[i] = f(a[2*i],a[2*i+1])
        r[N/2 + i] = f(b[2*i],b[2*i+1])
        }
    AVX version acts as applying SSE version to each half of the vectors
      A consequence of implementing AVX using 128-bit pipelines
        for(i in 0..N/4-1) {
        r[i] = f(a[2*i],a[2*i+1])
        r[N/4 + i] = f(b[2*i],b[2*i+1])
        r[N/2 + i] = f(a[N/2 + 2*i],a[N/2 + 2*i+1])
        r[N*3/4 + i] = f(b[N/2 + 2*i],b[N/2 + 2*i+1])
        }
      Effectively swaps the middle two quarters wrt. the naturally expected behavior
    There is no AVX512 version, operands must be first split into pairs of AVX vectors

## Slide 34: Vector instructions (SSE/AVX/AVX512)
Inter-lane shuffles
  Movement of data between lanes
  BEWARE: Most AVX/AVX512 shuffle instructions cannot move data between the 128-bit halves/quarters of the vectors
    Consequence of the original implementation using 128-bit pipelines
    Use permute2f128 for movement across AVX halves, permute4f128 for AVX2
    A vector-wide shuffle must be combined from permute and a 128-wide shuffle
  *alignr_epi8 – byte-granular shift right
    concatenate two 128-bit vectors, then pick 128 bits at the specified location
    the shift amount must be a constant (embedded into the instruction)
  AVX512: *alignr_epi(32|64) – 4/8-byte-granular shift right
    works smoothly across 128-bit boundaries
  *permute*, *shuffle* – “arbitrary” permutations
    unary cases
        for (i in 0..N-1) r[i] = a[p[i]]
    binary cases
        for (i in 0..N-1) r[i] = (p[i]&TOP_BIT) ? b[p[i]&LOW_BITS] : a[p[i]&LOW_BITS]
    many variants differing in granularity and other limitations
    most variants require permutation encoded in a constant, few accept run-time values

## Slide 35: Vector instructions (SSE/AVX/AVX512)
Conversions
  Changing widths of data; interaction with scalar registers
  *extract* - copy selected lane into a scalar register (or smaller vector register)
    the lane index must be a constant
  *insert* - copy a scalar value into a selected lane of a vector register
    the rest remains untouched, therefore there is an input vector too
    the lane index must be a constant
  *broadcast* - copy a scalar value (or a smaller vector) into all lanes
Pseudo-intrinsic functions (not single instructions) in C/C++
  *set1* - same as broadcast (where not in instruction set)
  *setzero* - set all lanes to zero
  *cast* - conversion between various vector forms (no runtime operation)

## Slide 36: Using MMX/SSE/AVX intrinsics in C/C++

## Slide 37: Using MMX/SSE/AVX intrinsics in C/C++
Intrinsic functions
  Formally declared in header files
  Recognized by the compiler
    Most intrinsic functions expand to one vector instruction
    Some functions are implemented using more than one scalar or vector instruction
  De-facto standard dictated by Intel and copied by MSVC, gcc, and others
Data types
  Declared in header files together with functions
  Names are standardized, but contents is different (use only as black boxes)
  Data types correspond to vector register types (widths)
        __m64, __m128, __m256, __m512
    For some type safety, there are three types for each width
      single-precision (no suffix)
      double-precision (suffix ‘d’)
      half-precision (suffix 'bh' for BF16 or 'h' for IEEE 754 Half)
      all integer widths (suffix ‘i’, except of __m64)

## Slide 38: Using MMX/SSE/AVX intrinsics in C/C++
header file | types | functions | technology
mmintrin.h | __m64 |  | MMX
xmmintrin.h | __m128 | _mm_*_ps | SSE
emmintrin.h | __m128d, __m128i | _mm_*_pd _mm_*_ep(i¦u)(8¦16¦32¦64) | SSE2
pmmintrin.h |  | _mm_*_p(s¦d) | SSE3
tmmintrin.h |  | _mm_*_epi(8¦16¦32) | SSSE3
smmintrin.h |  | _mm_*_* | SSE4.1
nmmintrin.h |  | _mm_cmp*, _mm_crc32_*, _mm_popcnt_u(32¦64) | SSE4.2
wmmintrin.h |  | _mm_aes*_si128 | 
immintrin.h | __m256, __m256d, __m256i | _mm256_* | AVX, AVX2
 | __m512, __m512d, __m512i | _mm512_* | AVX512
ammintrin.h |  | _mm_*, _mm256_* | AMD extensions

## Slide 39: Using MMX/SSE/AVX intrinsics in C/C++
Alignment
  It is recommended to align all vectors to 16 bytes. If not 16-byte aligned:
    SSE-only CPUs: segfault except for MOVUPS (loadu/storeu)
    AVX-enabled CPUs: reduced throughput, no segfault except for MOVAPS (load/store)
  It is advisable to align AVX2 vectors to 32 bytes and AVX512 vectors to 64 bytes
    avoid splitting over cache-line boundary (a split load counts as two loads)
  Compiler support
    When vector types are used for static or local variables or their parts, the compiler will align them
      Some compilers align to 16 and use MOVUPS, others align AVX to 32 and use MOVAPS
        __m256i v1; __m256i v2[4]; std::array<__m256i,4> v3; // everything aligned
    When vectors are simulated as arrays of scalar types, variables are unaligned
        std::int32_t v1[8]; // aligned only to 4 bytes!!!
      alignment may be enforced by alignas(16)
  Library support
    C++ library (containers, smart pointers) align correctly only since C++17
        std::vector<__m256i> v4; // aligned only to 8 bytes before C++17
    Before C++17 (or in C), alignment is done via semi-standardized functions
        _mm_malloc, posix_memalign, std::align

## Slide 40: Using MMX/SSE/AVX intrinsics in C/C++
Alignment
  alignas specifier
    Attached to class/struct types
        struct alignas(16) aligned_chunk { std::int32_t a[4]; };
    Attached to variables (including class/struct members)
        alignas(16) std::int32_t v1[8];
  Notes
    Alignment on dynamic allocation cannot be enforced when allocating primitive types
        std::vector<alignas(16) std::int32_t> // SYNTAX ERROR

## Slide 41: Using MMX/SSE/AVX intrinsics in C/C++
Vector-unaware data structures
        std::int32_t v1[40];
        std::vector<std::int32_t> v2;
    Aligned only to the scalar unit
    Requires reinterpret_cast for vector access
Vector-aware data structures
        __m256i v3[5];
        std::vector<__m256i> v4; // requires C++17 for proper alignment
    Correctly aligned data
    Requires reinterpret_cast for scalar access

## Slide 42: Using MMX/SSE/AVX intrinsics in C/C++
beware: reinterpret_cast may violate aliasing rules of C++
    Pointers to different types (unrelated by inheritance) are considered non-aliased
      Except the case of T* vs. char* (required for reading/writing binary files)
        __m256i* vector_data = /*...*/;
        vector_data[0] = /*...*/;
        std::int32_t* scalar_data = reinterpret_cast<std::int32_t*>(vector_data);
        /*...*/ = scalar_data[0];
      The compiler is allowed to reorder the vector store after the scalar read
  C++23: use std::launder
        __m256i* vector_data = /*...*/;
        vector_data[0] = /*...*/;
        std::int32_t* scalar_data = std::launder(reinterpret_cast<std::int32_t*>(vector_data));
        /*...*/ = scalar_data[0];
    The call to launder acts as a fence:
      Accesses through vector_data cannot be moved past the launder call
      Accesses through scalar_data cannot be moved before the launder call

## Slide 43: Using MMX/SSE/AVX intrinsics in C/C++
Correcting alignment at run time
    Determine alignment using (p % 16)
      requires reinterpret_cast to std::intptr_t
  When working on one unaligned array
    Initial and final unaligned elements processed in scalars, the rest in vectors
  When working on more unaligned arrays
    One of the arrays (preferably the output one) dictates alignment
      Write initial/final elements as scalars, the rest as vectors
    The other arrays:
      Either read/written unaligned (requires AVX-enabled CPUs)
      Or use alignr to extract the matching arguments from a pair of aligned vectors
    Problem: alignr requires a constant as the shift amount
      Code must be replicated for every possible value of alignment (may be too many)
      Complex templated machinery in C++ may be used
    Problem #2: AVX version of alignr works independently on 16-byte halves
      This is a consequence of (original) implementation using pipelined 128-bit ALU
      Use another instruction (permute2f128) before alignr