## Slide 1: The Example – CPU’s point of view

## Slide 2: Explanation
Branch prediction
  Virtual function call is an indirect branch
  Before determining the branch target, instruction can not be decoded
  CPU tries to predict the target
    Based on previous passes through the same instruction (at the same address)
      Associative memory (address of branch instruction -> target address)
      Heuristics, hardwired neural networks (AMD)
    Call-return pairs
  If prediction was wrong
    Decoded and partially executed instructions are dropped
    Decoding and execution of the correct instructions started from scratch
    Delay: in the magnitude of 10 CPU cycles

## Slide 3: Critical part of the code - Intel C++ 64-bit
Registers
  r14 = b
  r13 = e
  rcx = * b
  rax = VTable
  eax = value of f()
  rbp = stackframe
  [88+rbp] = s
Branches
  well predicted
    ret
    jne
  poorly predicted
    call
  Source code
        std::for_each( b, e, [&](A * p){ s += p->f(); });
  After procedure integration
        for(; b != e; ++ b) s += (*b)->f();
  Machine code of the loop
        .lp:
        mov rcx, QWORD PTR [r14]
        mov rax, QWORD PTR [rcx]
        call QWORD PTR [8+rax]
        add r14, 8
        add DWORD PTR [88+rbp], eax
        cmp r14, r13
        jne .lp ; Prob 82%
  Virtual function body
        mov eax, DWORD PTR [8+rcx]
        ret

## Slide 4: Critical part of the code - Intel C++ 64-bit
Dependencies
  write-read
  read-write
  test-access
Pipeline restart
  Wrongly predicted branch (into virtual function)
  Source code
        std::for_each( b, e, [&](A * p){ s += p->f(); });
  After procedure integration
        for(; b != e; ++ b) s += (*b)->f();
  Machine code of the loop
        .lp:
        mov rcx, QWORD PTR [r14]
        mov rax, QWORD PTR [rcx]
        call QWORD PTR [8+rax]
        add r14, 8
        add DWORD PTR [88+rbp], eax
        cmp r14, r13
        jne .lp ; Prob 82%
  Virtual function body
        mov eax, DWORD PTR [8+rcx]
        ret

## Slide 5: Critical part of the code - Intel C++ 64-bit
  Virtual function body
        mov eax, DWORD PTR [8+rcx]
        ret
  End of the loop
        add r14, 8
        add DWORD PTR [88+rbp], eax
        cmp r14, r13
        jne .lp ; Prob 82%
  Beginning of the loop
        .lp:
        mov rcx, QWORD PTR [r14]
        mov rax, QWORD PTR [rcx]
        call QWORD PTR [8+rax]
  Mispredicted branch target
        mov eax, DWORD PTR [4+rcx]
        ret
  Microops (guess)
        load eax,[8+rcx]
        load t1,[rsp++]
        jmp t1
        add r14,8
        load t2,[88+rbp]
        add t2,eax
        store [88+rbp],t2
        cmp r14,r13,eflags
        jne .lp,eflags
        load rcx,[r14]
        load rax,[rcx]
        load t3,[8+rax]
        store [--rsp],rip
        jmp t3
        load eax’,[4+rcx]
        load t4,[rsp++]
        jmp t4

## Slide 6: Executing code with misprediction
        1: load eax,[8+rcx]
        2: load t1,[rsp++]
        3: jmp t1
        4: add r14,8
        5: load t2,[88+rbp]
        6: add t2,eax
        7: store [88+rbp],t2
        8: cmp r14,r13,eflags
        9: jne .lp,eflags
        10: load rcx,[r14]
        11: load rax,[rcx]
        12: load t3,[8+rax]
        13: store [--rsp],rip
        14: jmp t3
        1': load eax’,[4+rcx]
        2': load t4,[rsp++]
        3': jmp t4
 | fetch+decode | load | ALU | retire+store
0 | 1..3 |  |  | 
1 | 4 |  |  | 
2 | 5..7 |  |  | 
3 | 8..9 |  |  | 
4 | 10..14 |  |  | 
5 | 1'..3' |  |  | 
6 |  | 1 |  | 
7 |  | . 2 | 4 | 
8 |  | . . 5 |  | 
9 |  | . . | 8 | 1
10 |  | . 10 |  | 2..4
11 |  | . 16 | 6 | 5
12 |  | . . |  | 6..9
13 |  | . 11 |  | 10
14 |  | . 1' |  | 
15 |  | . . |  | 
16 |  | . 12 |  | 11
17 |  | . 2' |  | 
18 |  | . . |  | 
19 |  | . |  | 12..14

## Slide 7: The same code with successful prediction
        1: load eax,[8+rcx]
        2: load t1,[rsp++]
        3: jmp t1
        4: add r14,8
        5: load t2,[88+rbp]
        6: add t2,eax
        7: store [88+rbp],t2
        8: cmp r14,r13,eflags
        9: jne .lp,eflags
        10: load rcx,[r14]
        11: load rax,[rcx]
        12: load t3,[8+rax]
        13: store [--rsp],rip
        14: jmp t3
 | fetch+decode | load | ALU | retire+store
0 |  | 1 | 4 | 
1 |  | . 2 | 8 | 
2 |  | . . 5 |  | 
3 |  | . . 10 |  | 1
4 |  | . . |  | 2..4
5 |  | . | 6 | 5
6 |  | 11 |  | 6..9
0 |  | . 1’ | 4’ | 10
1 |  | . . 2’ | 8’ | 
2 |  | . .12 |  | 11
3 |  | . . 5’ |  | 
4 |  | . . 10’ |  | 
5 |  | .. |  | 12..14
6 |  | . | 6’ | 1’..4’
7 |  | 11’ |  | 5’..8’
0 |  | . 1’’ | 4’’ | 9’-10’
1 |  | . . 2’’ | 8’’ | 
2 |  | . . 12’ |  | 11’
3 |  | . . 5’’ |  | 
4 |  | . . 10’’ |  | 

## Slide 8: Column-oriented implementation - example
        vector< int> data3d1;
        vector< int> data3d2;
        vector< int> data3d3;
        vector< int> data5d1;
        vector< int> data5d2;
        vector< int> data5d3;
        vector< int> data5d4;
        vector< int> data5d5;
        int s = 0;
        s += std::reduce( data3d2.begin(),
        data3d2.end(), 0, std::plus<int>());
        s += std::reduce( data5d3.begin(),
        data5d3.end(), 0, std::plus<int>());
No classes at all
Just arrays of elementary types
  Extremely difficult and error-prone
  No support for generic programming in this style
For each column, data are dense
  Improves cache behavior for column-oriented access
  Degrades cache behavior for row-oriented access
  Allows vectorization
    std::reduce [C++17] allows compilers to vectorize automatically
    The experiments were done with manual vectorization

## Slide 9: Column-organized data – problems of vectorization
    Column-stored data
        vector< int> data3d2;
    Non-vectorized naive code
        int s = 0;
        for ( auto && x : data3d2 )
        s += x;
    Good compilers can vectorize this code automatically
    There is no guarantee that vectorization is actually done
    Manual vectorization may be required to ensure performance
SIMD instructions
  Intel/AMD: MMX/SSE/AVX2/AVX512
Automatic vectorization
  Compilers generate vector instructions automatically
  Hints from programmers needed
Manual vectorization
  Library functions corresponding to individual vector instructions
    Knowledge of vector instruction set required
Problem: Alignment
  SIMD operations prefer/require aligned memory operands
  Alignment to 16B or more
Problem: Remainders at the end of the arrays
  Enlarged loop overhead
  Inefficient for small arrays

## Slide 10: Column-organized data – SSE3
        #include <emmintrin.h>
    Column-stored data in SSE types
        vector< __m128i> data3d2;
      Size of the unused space at the end
        std::size_t reserve3;
    Sum the vectors
        const __m128i * p = data3d2.data();
        const __m128i * e1 = p + data3d2.size() - 1;
        __m128i ss = 0;
        for (; p < e1; ++ p)
        ss = _mm_add_epi32( ss, *p);
        ss = _mm_hadd_epi32(ss,ss);
        ss = _mm_hadd_epi32(ss,ss);
        int s = mm_extract_epi32(ss, 0);
    Add the remaining scalars
        const int * q = (const int*)p;
        const int * e = q + 4 – reserve3,
        for (; q < e; ++ q)
        s += *q;
Intel intrinsics
          https://software.intel.com/sites/landingpage/IntrinsicsGuide/
  Header files + support inside compilers
    Available in all major C/C++ compiler suites
  Intrinsic functions
    A function for every instruction
      Compiler replaces function calls with the respective instructions
    Compiler handles register allocation, control-flow, scheduling etc.
      Using intrinsics is far easier than assembly language programming
Example
    __m128i is a 128-bit type corresponding to a SSE register
    _mm_add_epi32 is the SIMD instruction PADDQ
      4 additions of 32-bit integers
    _mm_hadd_epi32 = PHADDQ
      horizontal addition
    _mm_extract_epi32 = PEXTRD
      extract scalar from vector

## Slide 11: Column-organized data – SSE3
        #include <emmintrin.h>
    Column-stored data in SSE types
        vector< __m128i> data3d2;
      Size of the unused space at the end
        std::size_t reserve3;
    Sum the vectors
        const __m128i * p = data3d2.data();
        const __m128i * e1 = p + data3d2.size() - 1;
        __m128i ss = 0;
        for (; p != e1; ++ p)
        ss = _mm_add_epi32( ss, *p);
        ss = _mm_hadd_epi32(ss,ss);
        ss = _mm_hadd_epi32(ss,ss);
        int s = mm_extract_epi32(ss, 0);
    Add the remaining scalars
        const int * q = (const int*)p;
        const int * e = q + 4 – reserve3,
        for (; q != e; ++ q)
        s += *q;
    _mm_add_epi32 = PADDQ
      4 additions of 32-bit integers
    _mm_hadd_epi32 = PHADDQ
      “horizontal addition”
      significantly slower than PADDQ
    _mm_extract_epi32 = PEXTRD
      extract scalar from vector
+
+
+
+
+
+
+
+