## Slide 1: Computer Systems
CPU
Jakub Yaghob

## Slide 2: Von Neumann architecture
Simple, slower
CPU
Memory
I/O

## Slide 3: Harvard architecture
Microcontrollers
Multiple address spaces
CPU
Instruction Memory
Data Memory
I/O

## Slide 4: Real PC architecture
Sandy Bridge
mouse
LAN
Lan
Adap
South Bridge (PCH)
Audio Codec
DVD
Drive
Hard
Disk
Parallel Port
Serial Port
Floppy
Drive
PS/2 keybrd/ mouse
Cache
DDRIII
Channel 1
Mem BUS
DDRIII
Channel 2
Memory controller
Core
Core
D-sub, HDMI, DVI, Display port
External Graphics
Card
PCI express ×16
GFX
Display link
2133-1066 MHz
Line in
Line out
S/PDIF in
S/PDIF out
Super I/O
LPC
USB
SATA
SATA
BIOS
PCI express ×1
exp
slots
System Agent
4×DMI

## Slide 5: CPU
Architecture
  HW
  ISA
"Simple" machine
  Executes instructions
    Instruction – simple command

## Slide 6: Instructions - motivation
How can we execute the following code?
  if(a<3) b = 4; else c = a << 2;
  for(int i=0;i<5;++i) a[i] = i;
  int f(int p) { return p+1; }
  void g() { auto r = f(42); }

## Slide 7: Instruction classes
Load instructions
Store instructions
Move instruction
Arithmetic and logic instructions
Jumps
  Unconditional x conditional
  Direct x indirect x relative
Call, return
…

## Slide 8: Registers
Types
  General, integer, floating point, address, branch, flags, predicate, application, system, vector, …
Naming
  Direct x stack
Aliasing

## Slide 9: Registers – example 32-bit x86
EAX | AX | AH | AL |  | CS |  |  | 
EBX | BX | BH | BL |  | DS |  |  | 
ECX | CX | CH | CL |  | ES |  |  | 
EDX | DX | DH | DL |  | SS |  |  | 
ESI |  | SI |  |  | FS |  |  | 
EDI |  | DI |  |  | GS |  |  | 
EBP |  | BP |  |  | EFLAGS |  | FLAGS | 
ESP |  | SP |  |  | EIP |  | IP | 

## Slide 10: Registers – example IA-64

## Slide 11: MIPS – simple assembler
Execution environment
  32-bit registers r0-r31
    r0 is always 0, writes are ignored
    r31 is a link register for the jal instruction
  No stack
  No flags
  PC register

## Slide 12: MIPS – register aliases
Register | Name | Purpose | Preserve
$r0 | $zero | 0 | N/A
$r1 | $at | Assembler temporary | No
$r2-$r3 | $v0-$v1 | Return value | No
$r4-$r7 | $a0-$a3 | Function arguments | No
$r8-$r15 | $t0-$t7 | Temporaries | No
$r16-$r23 | $s0-$s7 | Saved temporaries | Yes
$r24-$r25 | $t8-$t9 | Temporaries | No
$r26-$r27 | $k0-$k1 | Kernel registers – DO NOT USE | N/A
$r28 | $gp | Global pointer | Yes
$r29 | $sp | Stack pointer | Yes
$r30 | $fp | Frame pointer | Yes
$r31 | $ra | Return address | Yes

## Slide 13: MIPS – instructions
Arithmetic
  add $rd,$rs,$rt
    R[rd] = R[rs]+R[rt]
  addi $rd,$rs,imm16
    R[rd] = R[rs]+signext(imm16)
  sub $rd,$rs,$rt
  subi $rd,$rs,imm16

## Slide 14: ISA comparison
MIPS
ADD $t1,$t1,$t0
ADDI $t1,$t1,1
ADD $t2,$t0,$t1
x86
ADD eax,ebx
ADD eax,1
MOV eax,ebx
ADD eax,ecx

## Slide 15: MIPS – instructions
Logic operations
  and/or/xor/nor $rd,$rs,$rt
  andi/ori/xori $rd,$rs,imm16
    R[rd] = R[rs] and/or/xor zeroext(imm16)
  No not instruction, use nor $rd,$rs,$rs
Shifts
  sll/slr $rd,$rs,shamt
    R[rd] = R[rs] << / >> shamt
  sra $rd,$rs,shamt

## Slide 16: ISA comparison
MIPS
NOR $t1,$t2
SLL $t1,$t1,3
x86
MOV eax,ebx
NOT eax
SHL eax,3

## Slide 17: MIPS – instructions
Memory access
  lw $rd,imm16($rs)
    R[rd] = M[R[rs] + signext32(imm16)]
  sw $rt,imm16($rs)
    M[R[rs] + signext32(imm16)] = R[rt]
  lb $rd,imm16($rs)
    R[rd] = signext32(M[R[rs] + signext32(imm16)])
  lbu $rd,imm16($rs)
    R[rd] = zeroext32(M[R[rs] + signext32(imm16)])
  sb $rt,imm16($rs)
    M[R[rs] + signext32(imm16)] = R[rt]
Moves
  li $rd,imm32
    R[rd] = imm32
  move $rd,$rs
    R[rd] = R[rs]

## Slide 18: ISA comparison
MIPS
LW $t1,1234($t0)
SW $t1,1234($t0)
LB $t1,1234($t0)
LI $t1,5678
MOVE $t1,$t0
x86
MOV eax,[ebx+1234]
MOV [ebx+1234],eax
MOV al,[ebx+1234]
MOV eax,5678
MOV eax,ebx

## Slide 19: MIPS – instructions
Jumps
  j addr
    PC = addr
  jr $rs
    PC = R[rs]
  jal addr
    R[31] = PC+4; PC = addr

## Slide 20: ISA comparison
MIPS
J label
JR $ra
JAL fnc
x86
JMP label1
JMP [ebx]
CALL fnc

## Slide 21: MIPS – instructions
Conditional jumps
  beq $rs,$rt,addr
    If R[rs]=R[rt] then PC=addr else PC=PC+4
  bne $rs,$rt,addr
Testing
  slt $rd,$rs,$rt
    If R[rs]<R[rt] then R[rd] = 1 else R[rd] = 0
  sltu $rd,$rs,$rt
    Unsigned version
  slti $rd,$rs,imm16
    If R[rs]<signext(imm16) then R[rd] = 1 else R[rd] = 0
  sltiu $rd,$rs,imm16
    If R[rs]<zeroext(imm16) then R[rd] = 1 else R[rd] = 0

## Slide 22: ISA comparison
MIPS
BEQ $t0,$t1,label
SLT $t2,$t1,$t0
BNE $t2,$zero,label
SLTI $t2,$t1,5
BNE $t2,$zero,label
x86
CMP eax,ebx
JZ label
CMP eax,ebx
JL label
CMP eax,5
JL label

## Slide 23: Flags
Only used by some ISA
Control execution
Check status of the last instruction
Usual flags
  Z – zero flag
  S – sign flag
  C – carry flag

## Slide 24: CPU
Architecture
  Memory controller
  Cache hierarchy
  Core
  Registers
    Types
  Logical processor
    Hyper threading
  Instructions

## Slide 25: Instruction
Simple command to the CPU
Encoding
Assembler
Operands
Instruction flow
  PC
Stack?
  SP

## Slide 26: ISA
Instruction set architecture
  Abstract model of CPU
Classification
  CISC – Complex Instruction Set Computer
  RISC – Reduced Instruction Set Computer
  VLIW – Very Long Instruction Word
  EPIC – Explicitly Parallel Instruction Computer
Orthogonality
  Accumulator
Load-Execute-Store

## Slide 27: CPU – simplified scheme
CORE 0
T0
T4
EU
L1I
L1D
L2
CORE 1
T1
T5
EU
L1I
L1D
L2
CORE 2
T2
T6
EU
L1I
L1D
L2
CORE 3
T3
T7
EU
L1I
L1D
L2
L3/LLC
Package

## Slide 28: Real CPU scheme – package
Intel Coffee Lake

## Slide 29: Real CPU scheme – core

## Slide 30: Real CPU die

## Slide 31: CPU architecture – pipeline
Current CPU
  14-19 stages

## Slide 32: CPU architecture – superscalar processor
Current CPU
  5-way, asymmetric

## Slide 33: CPU architecture – out-of-order execution
Decoder
Reservation station (pool)
µOPs
I/V ALU
Port 0
Port 1
Port 5
Port 6
Port 2
Port 3
Port 4
Port 7
I/V ALU
AGU
AGU
AGU
I ALU
I/V ALU
AGU
Load
Load
I Logic
Branch
I/F DIV
SQRT
AES
F FMA
String
I/V Logic
I/V MUL
F FMA
Bit scan
I/V Logic
I/V MUL
Comp Int
F ADD
Vec Shuff
Store
Branch
Reorder buffer